## Slide 1: Accelerating Systems with Programmable Logic Components Lecture 03 FPGAs + Verilog I
1DT109 ASPLOC
2022 VT1-VT2
Yuan Yao, yuan.yao@it.uu.se

## Slide 2: Agenda
Introduction to PLD and FPGAs
  PLD
  FPGA and its enablers
  Know your MINIZED board
  FPGA design flow
Verilog I
  Introduction to Verilog
  Gate-level modeling using Verilog
  Data-flow/RTL-level modeling using Verilog

## Slide 3: Introduction to PLD and FPGAs

## Slide 4: Need for programmable logic devices (PLD)
PROM – early 70’s
EPROM – early 70’s
PLA – mid 70’s
PAL – late 70’s
EEPROM – early 80’s

## Slide 5: Programmable Read-Only Memory (PROM)
Programmable Read-Only Memory (PROM) - early 70’s
  Address-line used as inputs (in canonical normal form)
  The value stored at an address defines the output for the specified input
  One-time programmable (OTP) using fuse/anti-fuse

## Slide 6: A PROM example
Address |  | Data |  |  | 
A0 | A1 | D3 | D2 | D1 | D0
0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 0 | 0 | 1
1 | 1 | 0 | 0 | 1 | 0

## Slide 7: Erasable PROM (EPROM)
Erasable PROM (EPROM)
  Erased by Ultraviolet light
  An Intel 1702A EPROM, one of the earliest EPROM types (1971), 256 by 8 bit.
  The small quartz window admits UV light for erasure.
BIOS in old PCs

## Slide 8: Programmable logic array (PLA)
Mid 1970’s
Programmable AND and OR gates matrices (planes)
Flexible
  Support large number of functions
Expensive
Slow
Hard to program

## Slide 9: Programmable array logic (PAL)
Late 1970’s
Programmable AND and fixed OR gates
Less flexible
  Support limited number of functions
Cheap
Fast
Hard to program but easier than PLA
Electronical world always welcomes cheap and fast things.

## Slide 10: Electronically EPROM (EEPROM)
Early 80’s
Breakthrough in PLD
Metal + Oxide + Semi-conductor = MOS
Breakthrough in information storage
  Flexible
  Cheap
  Fast
  Easy to program
Metal
(Semi
nowadays)
Oxide
Semi-conductor

## Slide 11: EEPROM: Write the “1” bit
(High voltage)
(High voltage)
Can last for 10+ years!

## Slide 12: EEPROM: Write the “0” bit
(High voltage)
(Low voltage)

## Slide 13: Field Programmable Gate Array (FPGA)
Mid 80’s
Xilinx co-founders Ross Freeman and Bernard Vonderschmitt invented the first commercially viable field-programmable gate array in 1985 – the XC2064.
64 logic blocks only

## Slide 14: FPGA – Xilinx timeline
1985: View and configure logic and routing resources manually
  “High-level” features such as Boolean expressions, K-maps, truth-tables, etc
1986: Automatic transition from schematic to physical (automatic placing & routing)
  We will learn how EDA plays a routing algorithm in Lecture 7
1995: Hardware Description Languages (HDL)

## Slide 15: FPGA - Architecture
Overall idea: Connecting simple but distributed reconfigurable units (called logic blocks) together towards complicated functions.

## Slide 16: FPGA – Configurable Logic Block (CLB)
The Look Up Table (LUT) can implement any function for the input combinations.
The Flip-Flop (FF) is used for store the result of the LUT.
The Mux can implement the CLB as combinational or sequential logic.

## Slide 17: CLB - LUT
Core of the FPGA architecture.
Change the contents of the SRAM to define outputs for different input patterns.
A | B | C | Output
0 | 0 | 0 | SRAM0
0 | 0 | 1 | SRAM1
0 | 1 | 0 | SRAM2
0 | 1 | 1 | SRAM3
1 | 0 | 0 | SRAM4
1 | 0 | 1 | SRAM5
1 | 1 | 0 | SRAM6
1 | 1 | 1 | SRAM7
0
1
0
1
0
1
0
1
0
1
0
1
0
1
How to implement 2-bits output functions for input A,B,C?
LUT
Write into mem to reconfigure LUT.

## Slide 18: How to implement the following function using the CLB we introduced?
A | B | C | O1 | O2
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 1
Using Two LUTs across Two CLBs!

## Slide 19: Implement O1 in CLB1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
1
1
0
1
1
0
1
0
A | B | C | O1 | O2
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 1
O1
LUT in CLB1

## Slide 20: Implement O2 in CLB2
0
1
0
1
0
1
0
1
0
1
0
1
0
1
1
0
1
0
1
1
0
0
A | B | C | O1 | O2
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 1
O2
LUT in CLB2

## Slide 21: Connecting CLB1 and CLB2
Connecting CLBs can only be done using the programmable interconnect, which resides outside the CLBs.
O1
O2
A B C
CLB2
CLB1

## Slide 22: FPGA - programmable interconnect
Programmable switch matrices (PSMs)
Connecting CLBs
Are reconfigurable themselves!

## Slide 23: Switch matrix interconnect point
With a 6-bit memory bitfield, 6 switched can be controlled at one intersection. Hence, all connection possibilities can be achieved.
M0 | M1 | M2 | M3 | M4 | M5 | 
0 | 0 | 0 | 0 | 0 | 1 | a-b
0 | 0 | 0 | 0 | 1 | 0 | b-d
0 | 0 | 0 | 1 | 0 | 0 | a-d
0 | 0 | 1 | 0 | 0 | 0 | a-c
0 | 1 | 0 | 0 | 0 | 0 | c-d
1 | 0 | 0 | 0 | 0 | 0 | b-d
Write into mem to reconfigure connections.

## Slide 24: FPGA – I/O blocks
Tri-state gate.
In the output mode, the output buffer is switched on and the input buffer switched off.
In the input mode, the output buffer is switched off and the input buffer switched on.

## Slide 25: FPGA – past and now
 | Xilinx XC2064 | Xilinx XCVU440 | Xilinx Zynq 7Z007S
Logic cells | 64 | 4.4M | 23K
CLB Flip-Flops | 64 | 5.0M | ??
Total Block RAM | 0 | 88.6Mb | 1.8Mb
DSP Slices | 0 | 2880 | 0
Maximum Number of I/O Pins | 38 | 1456 | 54
Differential Multi-Gigabit Transceivers | 0 | 48 | 0
Still, compared to ASICs:
FPGAs require 20-35x more area
10x more power
But 3-4x slower
But FPGAs are cheap and easy/quick to do implementation!

## Slide 26: The MINIZED starter kit board
Flash
Mem
Boot Loader Flash
FPGA
PS
PL

## Slide 27: FPGA applications
Test and prototyping before ASIC
Low-volume production (military, space, etc)
Accelerators (PS+PL)
Resilience to cosmic radiation (re-programmability)
From https://forums.xilinx.com/t5/Xilinx-Xclusive-Blog/Touchdown-NASA-s-Perseverance-Rover-Lands-on-Mars-with-Xilinx/ba-p/1209732
Hello MARS...Congratulations to the amazing engineers and scientists at NASA and Jet Propulsion Labs (JPL) for a successful touchdown on the Mars Jezero Crater on February 18, 2021! We are so proud to be part of this mission with Xilinx FPGAs in the lander rover and instruments, including the vision processor to perform image processing optimization for the historic first images.

## Slide 28: FPGA design flow
Schematic entry
Design deploying to FPGA
Program FPGA
Test FPGA In-System
Debug
Early Days
HDL & Graphic entry
Functional verification
Synthesis
Map & Place & Routing
Timing verification
Program & System test
Debug
Today
Debug
Debug

## Slide 29: Verilog I

## Slide 30: Introduction to Verilog HDL
Verilog is a Hardware Description Language (HDL)
A hardware description language is a language used to describe a digital system
Why using an HDL?
  Design abstraction: HDL v.s. layout by human
  Reduce cost and time to design hardware
  Design reuse (IPs)

## Slide 31: Brief history of HDLs
Late 70’s and early 80’s
  ISP, HiLo, PALASM, CUPL, ABEL, etc
  1971: Notion of “Register Transfer Level” (RTL) modeling
Mid 80’s:
  Verification & Logic (Verilog) by Gateway Design Automation
    C-like simulation language
    1989: Cadence acquires Gateway Design Automation
    1990: Verilog in public domain
  Very High-speed integrated circuit hardware Description Language (VHDL) by US Department of Defense
    Ada-like syntax
    Used for documentation and simulation
All require working with Boolean functions to some extent.
Better abstraction!

## Slide 32: Think in hardware, not in software
Verilog is for hardware modeling/specification
The model/specification can be simulated and then synthesized into hardware
Think in hardware!
  Explicit notion of time/concurrency
  Data-flow
C
a=1;
b=2;
c=0;
a=b; // a=b=2
c=a; // c=a=b=2
Compiled to the following
sequential instructions:
Load %a, %b
Load %c, %a
Result: c=a=b=2
Verilog
a=1;
b=2;
c=0;
a <= b; // a=b=2
c <= a; // c=a=1
Synthesized to the following
concurrent hardware structure:
// Synthesize the design in Vivado
Result: c=1, a=b=2;
Think in hardware.
Schema come first than code.

## Slide 33: Demo 1
Blocking/non-blocking assignments.
Verilog
//demo_1
a=1;
b=2;
c=0;
a <= b; // a=b=2
c <= a; // c=a=1
Synthesized to the following
concurrent hardware structure:
// Synthesize the design in Vivado
Result: c=1, a=b=2;
Verilog
//demo_2
a=1;
b=2;
c=0;
a = b; // a=b=2
c = a; // c=a=2
Synthesized to the following
concurrent hardware structure:
// Synthesize the design in Vivado
Result: c=a=b=2;

## Slide 34: Verilog supports various levels of abstraction
Behavioral model
Data flow model or register transfer level (RTL) model
Gate level model
Switch level model or transistor level model
Less detail (relying more on EDA)
Faster simulation
Shorter time-to-market
Less optimization
More detail (relying less on EDA)
Slower simulation
Longer time-to-market
More optimization

## Slide 35: In more detail, verilog can model…
Constructs used only for simulation
  Gate delays
  Signal strength
  Verilog procedural interface (VPI)
  Facilities for debugging/verification
  ...
Constructs used for both simulation and synthesis
  Registers
  Wires
  Assignments
  Operators
  …
Use synthesizable constructs for HW implementation.
Use non-synthesizable constructs for verification/debugging.

## Slide 36: Verilog example (digital design recap)
Implement the following function use Verilog
A | B | C | O
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Let us start with gate-level modeling.

## Slide 37: Step 1 – Schema comes first than code
And1
And2
A
B
C
O
my_module
Or1
Not1

## Slide 38: Step 2 – Model the module using gale-level Verilog
module my_module(A, B, C, O);
input A, B, C;
output O;
not Not1();
and And1();
and And2();
or Or1();
endmodule
And1
And2
A
B
C
O
my_module
Or1
Not1
my_module
declaration
input/output
sub module
Gate primitives provided in libraries:
GateName (out, in1, in2, in3, ... )

## Slide 39: Step 3 – connecting submodules up
module my_module(A, B, C, O);
input A, B, C;
output O;
not Not1(.in1(C));
and And1(.in1(A));
and And2(.in1(B), .in2(C));
or Or1(.out(O));
endmodule
Gate primitives provided in libraries:
GateName (out, in1, in2, in3, ... )
And1
And2
A
B
C
O
my_module
Or1
Not1
module my_module(A, B, C, O);
input A, B, C;
output O;
not Not1();
and And1();
and And2();
or Or1();
endmodule

## Slide 40: Step 3 – connecting submodules up
And1
And2
A
B
C
O
my_module
Or1
Not1
module my_module(A, B, C, O);
input A, B, C;
output O;
wire w_not, w_and1, w_and2;
not Not1(.in1(C));
and And1(.in1(A));
and And2(.in1(B), .in2(C));
or Or1(.out(O));
endmodule
Gate primitives provided in libraries:
GateName (out, in1, in2, in3, ... )
internal signal
Wires are used for connecting different elements. They can be treated as physical wires.

## Slide 41: Step 3 – connecting submodules up
And1
And2
A
B
C
O
my_module
Or1
Not1
module my_module(A, B, C, O);
input A, B, C;
output O;
wire w_not, w_and1, w_and2;
not Not1(.out(w_not), .in1(C));
and And1(.in1(A), .in2(w_not));
and And2(.in1(B), .in2(C));
or Or1(.out(O));
endmodule
Gate primitives provided in libraries:
GateName (out, in1, in2, in3, ... )
internal signal
w_not

## Slide 42: Step 3 – connecting submodules up
And1
And2
A
B
C
O
my_module
Or1
Not1
module my_module(A, B, C, O);
input A, B, C;
output O;
wire w_not, w_and1, w_and2;
not Not1(.out(w_not), .in1(C));
and And1(.out(w_and1), .in1(A), .in2(w_not));
and And2(.in1(B), .in2(C));
or Or1(.out(O), .in1(w_and1));
endmodule
Gate primitives provided in libraries:
GateName (out, in1, in2, in3, ... )
internal signal
w_and1

## Slide 43: Step 3 – connecting submodules up
And1
And2
A
B
C
O
my_module
Or1
Not1
module my_module(A, B, C, O);
input A, B, C;
output O;
wire w_not, w_and1, w_and2;
not Not1(.out(w_not), .in1(C));
and And1(.out(w_and1), .in1(A), .in2(w_not));
and And2(.out(w_and2), .in1(B), .in2(C));
or Or1(.out(O), .in1(w_and1), in2(2_and2));
endmodule
Gate primitives provided in libraries:
GateName (out, in1, in2, in3, ... )
internal signal
A lot of time on port mapping.
w_and2
Solution 1

## Slide 44: Port mapping by name vs by order
module my_module(A, B, C, O);
input A, B, C;
output O;
wire w_not, w_and1, w_and2;
not Not1(.out(w_not), .in1(C));
and And1(.out(w_and1), .in1(A), .in2(w_not));
and And2(.out(w_and2), .in1(B), .in2(C));
or Or1(.out(O), .in1(w_and1), in2(2_and2));
endmodule
module my_module(A, B, C, O);
input A, B, C;
output O;
wire w_not, w_and1, w_and2;
not Not1(w_not, C);
and And1(w_and1, A, w_not);
and And2(w_and2, B, C);
or Or1(O, w_and1, 2_and2);
endmodule
By name
By order
You can shuffle input/output order in named mapping, but not in order mapping.
Solution 2

## Slide 45: Any other way to do my_module?
Behavioral model
Data flow model or register transfer level (RTL) model
Gate level model
Switch level model or transistor level model
Less detail (relying more on EDA)
Faster simulation
Shorter time-to-market
Less optimization
More detail (relying less on EDA)
Slower simulation
Longer time-to-market
More optimization
Let’s do my_module in data-flow level.

## Slide 46: Data-flow level modeling
Step 1 – Schema comes first than code
And1
And2
A
B
C
O
my_module
Or1
Not1

## Slide 47: Step 2 – Model the module using data-flow level Verilog
module my_module(A, B, C, O);
input A, B, C;
output O;
wire w_not, w_and1, w_and2;
assign w_not = ~C;
assign w_and1 = A & w_not;
assign w_and2 = B & C;
assign O = w_and1 | w_and2;
endmodule
And1
And2
A
B
C
O
my_module
Or1
Not1
w_and1
w_and2
w_not
Signals of type wire requires the continuous assignment of a value. In Verilog, this concept is realized by the assign statement where any wire can be driven continuously with a value.
Solution 3

## Slide 48: Step 2 – Model the module using data-flow level Verilog
module my_module(A, B, C, O);
input A, B, C;
output O;
assign O = (A & ~C) | (B & C);
endmodule
Solution 4

## Slide 49: Step 2 – Model the module using data-flow level Verilog
module my_module(A, B, C, O);
input A, B, C;
output O;
assign O = (C) ? B : A;
endmodule
Solution 5
MUX
C
A
B
O
my_module is actually a way to implement multiplexer using gates.

## Slide 50: EDA Synthesis
The five solutions differ in coding style, complicity, readability, conciseness, etc
Choose wisely according to your project’s/teammates’ needs
All the four solutions yield the same synthesis result in Vivado.
Unlike in ASIC, you cannot see the gates but only LUTs in FPGA synthesis.
If you like, you can still see the “gates” under RTL analysis -> schematic.

## Slide 51: Questions?