## Slide 1: Accelerating Systems with Programmable Logic Components Lecture 04 Verilog II
1DT109 ASPLOC
2022 VT1-VT2
Yuan Yao, yuan.yao@it.uu.se
Courtesy to Philipp Rümmer

## Slide 2: Agenda
Review module-based modelling in Verilog
Combinational vs. sequential logic
Blocking vs. nonblocking assignment
Writing testbench using Verilog

## Slide 3: Module-based modelling in Verilog
module my_module(A, B, C, O);
input A, B, C;
output O;
wire w_not, w_and1, w_and2;
not Not1(.out(w_not), .in1(C));
and And1(.out(w_and1), .in1(A), .in2(w_not));
OR
assign O = (A & ~C) | (B & C);
endmodule
And1
And2
A
B
C
O
my_module
Or1
Not1
input/output port definition
connecting wire
gate-level modeling
data-flow level modeling
my_module
declaration
This is for combinational logic.

## Slide 4: Combinational vs Sequential logic
Combinational logic is defined as the time independent logic which do not depends upon previous inputs to generate any output.
  Examples – Encoder, Decoder, Multiplexer, Demultiplexer
Sequential logic is a type of logic circuit whose output depends not only on the present value of its input signals but on the sequence of past inputs, the input history as well.
  Examples – Flip-flops, counters, memory

## Slide 5: Sequential logic example: counter
Adder
(combinational logic)
Input
Output = Input + 1
Mem component
such as Flip-Flop
(sequential logic)
clk
Output = Cur + 1

## Slide 6: Sequential logic example: critical path break
Combinational logic
input
output
Delay=X > threshold
Combilogic
input
output
Delay=X/2 < threshold
FF
Delay=X/2 < threshold
Combilogic
Speed/area tread off.

## Slide 7: Model flip-flop (FF) using Verilog
D_FF
D
Q
clk
Step 1: Find the schema of an FF
Step 2: Use gate-level or data-flow level modeling for FF
Do we have other options?

## Slide 8: Model flip-flop (FF) using Verilog
We can use RTL-level modeling in Verilog to model FF
The recommended way to model combinational logic in Verilog
D_FF
D
Q
clk
module d_ff(clk, D, Q);
input clk, D;
output Q;
reg Q;
always @ (posedge clk) begin
Q <= D;
end
endmodule

## Slide 9: The always block
An always block is one of the procedural blocks in Verilog.
Statements inside an always block are executed sequentially.
But they may take effect simultaneously
a=1;
b=2;
always @ (a, b) begin
a <= b;
b <= a;
end // a=2, b=1;
a=1;
b=2;
always @ (a, b) begin
a = b;
b = a;
end // a=2, b=2;

## Slide 10: The sensitivity list
A sensitivity list is the expression that defines when the always block should be executed and is specified after the @ operator within parentheses ( ).
Sensitivity list is the key to differentiate combinational logic and sequential logic.
always @ (a, b)
begin
c = a | b;
end
always @ (posedge clk)
begin
c <= a | b;
end
Execute always block whenever value of “a” or “b” change – combinational logic
Execute always block only on the rising edge of signal clk – sequential lock
Rules of thumb No.1:
Put all input signals into the sensitivity list for combinational logic
Put only the clock (and reset if needed) signal into the sensitivity list for sequential logic
Can also use negedge
for falling edge

## Slide 11: The reg data type (vs wire)
Verilog data types are divided into two main groups: nets (wire) and variables (reg). The distinction comes from how they are intended to represent different hardware structures.
A net (wire) data type represents a physical connection between structural entities. (Recall the my_module example)
A variable (reg) data type represents a piece of storage.
Rules of thumb No.2:
Drive a Verilog wire with assign statement or port output
Drive a Verilog reg from an always block.
reg c;
always @ (a, b)
begin
c = a | b;
end
reg c;
always @ (posedge clk)
begin
c <= a | b;
end
wire c;
assign c = a | b;

## Slide 12: Demo 1
my_module from Verilog I using always block
module demo_1(A,B,C,O);
input A, B, C;
output O;
assign O = reg_o;
reg reg_o;
always @ (A, B, C) begin
reg_o = A & ~B | B & C;
end
endmodule
And1
And2
A
B
C
O
my_module
Or1
Not1

## Slide 13: Putting them all together
Q only reflects the value of D on a rising edge
  Rising edge means 0 in the past of input and 1 in the current
D_FF
D
Q
clk
module d_ff(clk, D, Q);
input clk, D;
output Q;
reg Q;
always @ (posedge clk) begin
Q <= D;
end
endmodule
Can also use non-clock signals as trigger

## Slide 14: D_FF with synchronous reset
Add a reset to the D_FF
Synchronous reset means that the D_FF can only be reset on clock edge (in our case, a rising edge)
module d_ff(clk, D, Q);
input clk, D;
output Q;
reg Q;
always @ (posedge clk) begin
if(!reset)
Q <= 1’b0;
else
Q <= D;
end
endmodule
D_FF
D
Q
clk
reset
Added gates!
How to add asynchronous reset?

## Slide 15: D_FF with asynchronous reset
Add a reset to the D_FF
Asynchronous reset means that the D_FF can be reset on reset edge (in our case, a falling edge)
module d_ff(clk, D, Q);
input clk, D;
output Q;
reg Q;
always @ (posedge clk, negedge reset) begin
if(!reset)
Q <= 1’b0;
else
Q <= D;
end
endmodule
D_FF
D
Q
clk
reset
Always use asynchronous D_FF.
It keeps your datapath shorter/faster.
(why???)
No added gates needed!

## Slide 16: Blocking vs. non-blocking assignment
Different ways to drive wire and reg.
= is called blocking assignment.
  Blocking assignment executes “in series” because a blocking assignment blocks execution of the next statement until it completes.
<= is called non-blocking assignment.
  Non-blocking assignment executes “in parallel” because it describes assignments that all occur at the same time.
reg c;
always @ (a, b)
begin
c = a | b;
end
reg c;
always @ (posedge clk)
begin
c <= a | b;
end
wire c;
assign c = a | b;
Blocking assignment
Non-blocking assignment
Rules of thumb No.3:
Use blocking assignment to model combinational logic.
Use non-blocking assignment to model sequential logic.
Bad styles can lead to both buggy and incorrect circuit.

## Slide 17: Blocking assignment – Good and bad styles
A
B
C
O
reg r_and, r_or;
assign O = r_or;
always @ (A, B, C) begin
r_and = A & B;
r_or = r_and | C;
end //demo_2
Good style
reg r_and, r_or;
assign O = r_or;
always @ (A, B, C) begin
r_and <= A & B;
r_or <= r_and | C;
end //demo_2
Bad style
Behavioral
Behavioral
Post-synth
Post-synth
Results
Match!
(no bug)
Results
Mismatch!
(bug in front-end)

## Slide 18: Non-blocking assignment – Good and bad styles
D_FF
D_1
clk
D_FF
D_2
Q
reg D_2, _Q;
assign Q = _Q;
always @ (posedge clk) begin
D_2 <= D_1;
_Q <= D_2;
end //demo_3
Good style
reg D_2, _Q;
assign Q = _Q;
always @ (posedge clk) begin
D_2 = D_1;
_Q = D_2;
end //demo_3
Bad style

## Slide 19: Design pitfalls
Multi drive always module
Combinational loop

## Slide 20: Multi-drive always blocks
Statements within always are evaluated sequentially from the first to the last.
However, different always blocks are executed randomly.
  The execution order of the green and blue always are totally random run-to-run.
always @ (a, b) begin
…
x = a | b;
…
end
always @ (c, d) begin
…
x = c & d;
…
end
Critical warning generated during synthesis.
Rules of thumb No.4:
Each reg should only be driven by one always block.

## Slide 21: Bit-vector is the only data type in Verilog
Vdd
Vdd
Vdd
Vss
Vss
Vss
A bit can take on one of four values
Value | Meaning
0 | Logic zero

## Slide 22: Bit-vector is the only data type in Verilog
Vdd
Vdd
Vdd
Vss
Vss
Vss
A bit can take on one of four values
Value | Meaning
0 | Logic zero
1 | Logic one

## Slide 23: Bit-vector is the only data type in Verilog
Vdd
Vdd
Vdd
Vss
Vss
Vss
A bit can take on one of four values
Value | Meaning
0 | Logic zero
1 | Logic one
Z | High impedance, floating

## Slide 24: Bit-vector is the only data type in Verilog
Value | Meaning
0 | Logic zero
1 | Logic one
Z | High impedance, floating
X | Unknown logic value
A bit can take on one of four values
An X bit might be a 0, 1, Z, or in transition. We can set bits to be X in situations where we don’t care what the value is. This can help catch bugs and improve synthesis quality (Lecture 5 – Verilog III).
Vdd
Vdd
Vdd
Vss
Vss
Vss

## Slide 25: Bit literals
Binary literals
  2’b01 (01)
  8’b0001_1111 (00011111)
  -3’b1 (111)
Octal literals
  6’o12 (001_010)
Hexadecimal literals
  6’h1f (01_1111)
  16’haxxz (1010_xxxx_xxxx_zzzz)
Decimal literals
  4’d1 (0001)
  -4’d1 (1111)
  reg[3:0] a = 1; (0001)
  reg[3:0] a = -1; (1111)
  integer a = 1; (0000_0000_..._0001, 32-bit)
  Integer a = -1; (1111_1111_..._1111, 32-bit)
4’b10_11
Base format
(B, O, H, D)
Decimal number
Representing size in bits
Underscores
are ignored

## Slide 26: Combinational loop – the obvious case
always @ (a, b)
begin
c = a | b;
end
always @ (a, b)
begin
c = a | b | c;
end //demo_4
Hard to use simulation results to detect combi-loop.
No error generated at both pre and post synthesis simulation.
But a non-critical warning is generated during synthesis.
Or an error message is generated during later bit stream generation.
Rules of thumb No.5:
Remember to check the Vivado methodology report at each step.

## Slide 27: Combinational loop – the covert case
always @ (a, x) begin
…
y = a| x;
…
end
always @ (y, b) begin
…
x = y | b;
…
end
y
x
A combi-loop may hide within the ocean of gates in a large design.

## Slide 28: Writing testbench using Verilog
Testbenches are used to test/debug Verilog design with synthetic inputs and collect the outputs.
Testbenches are usually top modules in a Verilog project.
  The design-under-test is a sub-modules in a testbench module
Testbenches are not supposed to be synthesizable.
testbench
DUT/UUT
inputs
outputs

## Slide 29: A testbench example
A
B
C
O
module demo_2(A, B, C, O);
input A, B, C;
output O;
reg r_and, r_or;
assign O = r_or;
always @ (A, B, C) begin
r_and = A & B;
r_or = r_and | C;
end
Endmodule
DUT.v
`timescale 1ns/1ps
module tb;
reg a, b, c;
wire o;
demo_2 UUT(a, b, c, o);
localparam period = 1;
initial begin
a = 0; b = 0; c = 0;
#period;
a = 1; b = 0; c = 0;
#period;
a = 1; b = 1; c = 0;
. . .
end
endmodule
tb.v
What we get from DUT.v
What we get from tb.v
Top module, no input nor outpus
Instantiation

## Slide 30: What defines a good testbench and how to achieve them
Input coverage
  As much different input patterns as possible
  Loop statement
Reliability
  Mimic the electronic properties of real-word signals
  Timing control
    Delay control
    Edge sensitive event control
    Level sensitive event control
    Named event (Lecture 9 – Verification)
Reusability/readability
  Functionalities encapsulation
  Function and task

## Slide 31: Loop statement
Verilog provides four ways to do loop
  for
  while
  repeat
  forever
Loop statements are synthesizable for iterations with finite values known at elaboration (compile) time
  Loop statements are synthesized with hardware replication
  Although possible but is it a bad practice
Loop statements are better match for test bench and verification

## Slide 32: For loop statement
`timescale 1ns/1ps
module tb;
reg a, b, c;
wire o;
demo_5 UUT(a, b, c, o);
localparam period = 1;
initial begin
a = 0; b = 0; c = 0;
#period;
a = 1; b = 0; c = 0;
#period;
a = 1; b = 1; c = 0;
. . .
end
endmodule
tb.v
Need 8 lines to exhaust all input patterns.
What if the input contains 16 signals?
216 lines!
`timescale 1ns/1ps
module tb;
reg [2:0] a;
wire o;
demo_5 UUT(a[2], a[1], a[0], o);
localparam period = 1;
integer i;
initial begin
for (i=0; i<8; i=i+1) begin
a = {i[2], i[1], i[0]};
#period;
end
end
endmodule
tb.v
3-bit reg “a”, with MSB at the most left.
assign bit a[2] to the first port of UUT, and so on. That is:
a[2] to a, A[1] to b, A[0] to c.
Interger data type (32-bit) i for loop counter.
The loop body
Wrap up the last three bits of i using “{}” and assign them all to a.
This is equivalent to:
a[2] = i[2], a[1] = i[1], a[0]=i[0];
The initial block is like the always block except that it is executed just once.

## Slide 33: While and repeat loop statements
`timescale 1ns/1ps
module tb;
reg [2:0] a;
wire o;
demo_5 UUT(a[2], a[1], a[0], o);
localparam period = 1;
integer i;
initial begin
i=0;
while (i < 8) begin
i = i + 1;
a = {i[2], i[1], i[0]};
#period;
end
end
endmodule
tb.v
Loop body
using
while
`timescale 1ns/1ps
module tb;
reg [2:0] a;
wire o;
demo_5 UUT(a[2], a[1], a[0], o);
localparam period = 1;
integer i;
initial begin
i=0;
repeat (8) begin
i = i + 1;
a = {i[2], i[1], i[0]};
#period;
end
end
endmodule
tb.v
Loop body
using
repeat

## Slide 34: Verilog operators
Operator | Name
[ ] | Bit-select
~ | Bit-Negation
& | Bit-AND
¦ | Bit-OR
~& | Bit-NAND
~¦ | Bit NOR
^ | Bit XOR
~^ or ~^ | Bit XNOR
Operator |  |  |  | Name
! |  |  |  | Logic-Negation
< | <= | >= | > | Logic-Comparison
== |  | != |  | Logic-Comparison
&& |  |  |  | Logic-AND
¦¦ |  |  |  | Logic-OR
? : |  |  |  | Logic-Conditional
Operator |  |  |  |  | Name
{ } |  |  |  |  | concatenate
{ { } } |  |  |  |  | replication
+ | - | * | / | % | Arithmetic
wire w_reduce;
assign w_reduce = ~&tmp[3:0]
module replication_operator();
reg [3:0] r_VAL_1 = 4'b0111;
parameter c_MULTIPLIER = 4'b0010;
initial
begin
// Replication Only
$display("Replication of 0x7, 3 times is 0x%h",
{3{r_VAL_1}} );
// Replication is possible using a constant (parameter)
// Note that replication multiplier CANNOT be a reg
$display("Replication of 0x7, %1d times is 0x%h",
c_MULTIPLIER, {c_MULTIPLIER{r_VAL_1}} );
// Replication and Concatenation together
$display("Concatenate 4 with replication of 0xA twice: 0x%h",
{4'h4,{2{4'hA}}} );
// Replication and Concatenation 2
$display("Replicate the concatenation of 0xB and 0xC 4 times: 0x%h",
{4{4'hB, 4'hC}} );
#20;
$finish;
end
endmodule // replication_operator
Notes: # Replication of 0x7, 3 times is 0x777
# Replication of 0x7, 2 times is 0x77
# Concatenate 4 with replication of 0xA twice: 0x4aa
# Replicate the concatenation of 0xB and 0xC 4 times: 0xbcbcbcbc
# ** Note: $finish : example_replication_operator.v(32)

## Slide 35: Verilog timing control
There are four types of timing controls in Verilog
  Delay control
  Edge sensitive event control
  Level sensitive event control
  Named events

## Slide 36: Delay control
# N: delay of N time units
Example:
Example 2
…
localparam period = 1;
integer i;
initial begin
i=0;
while (i < 8) begin
i = i + 1;
a = {i[2], i[1], i[0]};
#period;
end
end
endmodule
Delay can be controlled using local var.
Delay for 1 unit time at the end of each loop iteration.
Example 1
Example 3
…
localparam period = 5;
reg clk;
initial begin
clk=0;
forever begin
#period clk = ~clk;
end
end
endmodule
Clock generator
always begin
a = 1’b0;
#5;
a = 1’b1;
#3;
a=1’b0;
end

## Slide 37: Delay control – Time unit
`timescale time_unit base / precision base
The first argument specifies “#1” delay
The second argument specifies the how delay values are rounded
Base is in
  s 1s
  ms 1-3s
  us 1-6s
  ns 1-9s
  ps 1-12s
  fs 1-15s
Example
`timescale 1ns/1ns
Delay Meaning Sim. Time
#1 // Delay 1 ns 1
#0.49 // Delay 0 ns 1
#0.5 // Delay 1 ns 2
#0.51 // Delay 1 ns 3
#5 // Delay 5 ns 8

## Slide 38: Delay control – Gate delay
So far, we have assumed perfect signal response time
  It takes no time for signal to change from 0 to 1
  It takes no time for signal to change from 1 to 0
  This cannot be true in real life where the electronic properties of gates take effect
Three kinds of delays
  Rise delay The time taken for the output of a gate to change from 0,x,z, to 1 is called a rise delay.
  Fall delay The time taken for the output of a gate to change from 1,x,z, to 0 is called a fall delay.
  Turn-off delay The time taken for the output of a gate to change from 0,1,x, to z is called a turn-off delay.

## Slide 39: Delay control – Gate delay
Verilog uses # to control rise/fall/turn-off delay of signals
Let’t talk about gate delay of an “and” gate
  and and1(o,a,b) // Ideal “and” gate
  and #1 and1(o,a,b) // All delays
  and #(1,1) and1(o,a,b) // t_rise=1, t_fall=1
  and #(1,2,3) and1(o,a,b) // t_rise=1, t_fall=2, t_off=3
  and #(1:2:3,2:3:4,3:4:5) and1(o,a,b) // min:typ:max
Min |  |  | Typ |  |  | Max |  | 
t_rise | t_fall | t_max | t_rise | t_fall | t_max | t_rise | t_fall | t_max
1 | 2 | 3 | 2 | 3 | 4 | 3 | 4 | 5
The default choice
Gate delays are used in post-synthesis timing simulation, where only the gate delays of the gate library vendor are used.

## Slide 40: Gate delay example
module demo_6( input a, b, output out1, out2);
and #(1:2:3, 2:3:4) and1 (out1, a, b);
and and2 (out2, a, b);
endmodule
module tb;
reg a,b;
wire out1, out2;
demo_6 UUT(a, b, out1, out2);
initial begin
{a, b} <= 0;
#10 a <= 1;
#10 b <= 1;
#10 a <= 0;
#10 b <= 0;
end
endmodule
Pre-synthesis behavioral simulation
Post-synthesis timing simulation
2ns
0ns
3ns
0ns
~5ns
~5ns

## Slide 41: Edge sensitive event control
A statement happens only when the posedge and/or negedge event happens
Can be attached to sensitivity list of an “always” block always @ (posedge clk);
  Execute the always block at each rising edge of signal “clk”
Or to individual assignments @ (posedge clk) X <= Y;
  Delay assignment X<=Y until the positive edge of “clk”. X <= @ (posedge clk) Y;
  Read y immediately but delay the assignment to posedge “clk”.
At positive and/or negative edges @(posedge x and negedge y) @(posedge x or negedge y)

## Slide 42: Edge sensitive event control
module tb; //demo_7
reg clk;
reg [2:0] a, b, c, d;
initial begin
clk = 0;
forever begin
#5 clk = ~clk;
end
end
always begin
@(posedge clk) a=3'd1;
@(posedge clk) b=3'd2;
@(posedge clk) c=3'd3;
@(posedge clk) d=3’d4;
$display("time is %0t",$time);
end
endmodule
time is 35 ns
time is 75 ns
time is 115 ns
time is 155 ns
time is 195 ns
time is 235 ns
time is 275 ns
time is 315 ns
time is 355 ns
time is 395 ns
time is 435 ns
module tb; //demo_7
reg clk;
reg [3:0] a, b, c, d;
initial begin
clk = 0;
forever begin
#5 clk = ~clk;
end
end
always begin
@(posedge clk) a<=3'd1;
@(posedge clk) b<=3'd2;
@(posedge clk) c<=3'd3;
@(posedge clk) d<=3’d4;
$display("time is %0t",$time);
end
endmodule
time is 35 ns
time is 75 ns
time is 115 ns
time is 155 ns
time is 195 ns
time is 235 ns
time is 275 ns
time is 315 ns
time is 355 ns
time is 395 ns
time is 435 ns

## Slide 43: Level sensitive event control
@(X, Y)
  A block will be executed each time a variable changes its value
@* or @(*)
  A block will be executed at change of any variable that is read in its scope
  Always use blocking assignment “=” inside @*/@(*)
wait( )
  A block will be executed until a condition becomes true within the wait() function.

## Slide 44: Example of wait()
module tb;
reg [3:0] ctr;
reg clk;
initial begin
{ctr, clk} <= {4’b0000, 1’b0};
wait (ctr);
$display ("T=%0t Counter reached non-zero value 0x%0h", $time, ctr);
wait (ctr == 4’b0100)
$display ("T=%0t Counter reached 0x%0h", $time, ctr);
$finish;
end
always clk = #10 ~clk;
always @ (posedge clk)
ctr <= ctr + 1;
endmodule
Executed at simulation time 0. {ctr, clk} <=0
Executed at simulation time 0.
Executed at simulation time 0.
Blocked until ctr is non-zero.
Blocked for 10 UT.
Blocked until posedge clk.
10 UT: clk = 1
Blocked for 10 UT.
10 UT: ctr = 1
Wait for posedge.
10 UT: execute the first $display.
Blocked until crt is 4
70 UT: clk = 1
Blocked for 10 UT.
70 UT: ctr = 4
Blocked for 10 UT.
70 UT: execute the second $display.
Simulation finishes.
Initial block first
Trigger order
Trigger order
A hideous bug here
20 UT: clk = 0
Blocked for 10 UT.
Should be =, not <=
Notes: always clk = #10 ~clk;
Reads the unitialized value of clk at timestamp 0 since clk is assigned using non-blocking
Assignment in the initial block

## Slide 45: Verilog function vs task
Verilog provides function and task for code reuse.
Help to improve reusability readability in large projects.
They are similar but differ in many aspects.

## Slide 46: Verilog function vs task
Verilog provides function and task for code reuse.
Help to improve reusability readability in large projects.
They are similar but differ in many aspects.
 | Function | Task
1 | Do not allow initial or always block. | 

## Slide 47: Verilog function vs task
Verilog provides function and task for code reuse.
Help to improve reusability readability in large projects.
They are similar but differ in many aspects.
 | Function | Task
1 | Do not allow initial or always block. | 
2 | A function takes 0 simulation time to execute. | A task takes arbitrary simulation time to execute depending on the timing control statements within.

## Slide 48: Verilog function vs task
Verilog provides function and task for code reuse.
Help to improve reusability readability in large projects.
They are similar but differ in many aspects.
 | Function | Task
1 | Do not allow initial or always block. | 
2 | A function takes 0 simulation time to execute. | A task takes arbitrary simulation time to execute depending on the timing control statements within.
3 | A function cannot contain timing control statements such as: # delay, posedge, negedge, etc. | A task can contain timing control statements.

## Slide 49: Verilog function vs task
Verilog provides function and task for code reuse.
Help to improve reusability readability in large projects.
They are similar but differ in many aspects.
 | Function | Task
1 | Do not allow initial or always block. | 
2 | A function takes 0 simulation time to execute. | A task takes arbitrary simulation time to execute depending on the timing control statements within.
3 | A function cannot contain timing control statements such as: # delay, posedge, negedge, etc. | A task can contain timing control statements.
4 | A function can call other functions but can not call tasks. (Because of Rule 2 & 3) | A task can call other functions or tasks. (Because of rule 2 and 3)

## Slide 50: Verilog function vs task
Verilog provides function and task for code reuse.
Help to improve reusability readability in large projects.
They are similar but differ in many aspects.
 | Function | Task
1 | Do not allow initial or always block. | 
2 | A function takes 0 simulation time to execute. | A task takes arbitrary simulation time to execute depending on the timing control statements within.
3 | A function cannot contain timing control statements such as: # delay, posedge, negedge, etc. | A task can contain timing control statements.
4 | A function can call other functions but can not call tasks. (Because of Rule 2 & 3) | A task can call other functions or tasks. (Because of rule 2 and 3)
5 | A function must have at least one input argument but cannot have output arguments. | A task can have any number (zero or more) of input and output ports.

## Slide 51: Verilog function vs task
Verilog provides function and task for code reuse.
Help to improve reusability readability in large projects.
They are similar but differ in many aspects.
 | Function | Task
1 | Do not allow initial or always block. | 
2 | A function takes 0 simulation time to execute. | A task takes arbitrary simulation time to execute depending on the timing control statements within.
3 | A function cannot contain timing control statements such as: # delay, posedge, negedge, etc. | A task can contain timing control statements.
4 | A function can call other functions but can not call tasks. (Because of Rule 2 & 3) | A task can call other functions or tasks. (Because of rule 2 and 3)
5 | A function must have at least one input argument but cannot have output arguments. | A task can have any number (zero or more) of input and output ports.
6 | A function can return a single value. | A task cannot return a value but can achieve the same effect using output arguments.

## Slide 52: Verilog function vs task
Verilog provides function and task for code reuse.
Help to improve reusability readability in large projects.
They are similar but differ in many aspects.
 | Function | Task
1 | Do not allow initial or always block. | 
2 | A function takes 0 simulation time to execute. | A task takes arbitrary simulation time to execute depending on the timing control statements within.
3 | A function cannot contain timing control statements such as: # delay, posedge, negedge, etc. | A task can contain timing control statements.
4 | A function can call other functions but can not call tasks. (Because of Rule 2 & 3) | A task can call other functions or tasks. (Because of rule 2 and 3)
5 | A function must have at least one input argument but cannot have output arguments. | A task can have any number (zero or more) of input and output ports.
6 | A function can return a single value. | A task cannot return a value but can achieve the same effect using output arguments.
7 | A function can be called in an expression or can be called with a statement (disconnected function). (Because of Rule 5 and 6) | A task must be specifically called with a statement. (Because of Rule 5 and 6)
Rules of thumb No.6:
Use function to model combi-logic.
Use task to model either combi- or sequential logic.

## Slide 53
module has_task (x_in, rev_x); //demo_9
parameter maxbits = 8;
input [maxbits - 1 : 0] x_in;
output reg [maxbits - 1 : 0] rev_x;
task reverse_bits;
input [maxbits - 1 : 0] din;
output [maxbits - 1 : 0] dout;
integer k;
begin
for (k=0; k < maxbits; k = k +1)
dout[maxbits-1-k] = din[k];
end
endtask
always @ (x_in)
reverse_bits(x_in, rev_x);
endmodule
module has_function (x_in, rev_x); //demo_9
parameter maxbits = 8;
input [maxbits - 1 : 0] x_in;
output reg [maxbits - 1 : 0] rev_x;
function [maxbits - 1 : 0] reverse_bits;
input [maxbits - 1 : 0] din;
integer k;
begin
for (k=0; k < maxbits; k = k +1)
reverse_bits[maxbits-1-k] = din[k];
end
endfunction
always @ (x_in)
rev_x = reverse_bits(x_in);
endmodule
function name is the implicit output reg name.
Don’t declare your local reg with the same name!

## Slide 54: Questions?