## Slide 1: Accelerating Systems with Programmable Logic Components Lecture 08 Verification I Basic concepts and methods of Verification
1DT109 ASPLOC
2021 VT1-VT2
Yuan Yao, yuan.yao@it.uu.se

## Slide 2: Agenda
Introduction to Verification
  Verification model
  Verification abstraction
  Verification task
Introduction to SystemVerilog
  Basic building blocks
Delta delay

## Slide 3: The Quebec Bridge and Pierre Laporte Bridge
Cantilever bridge
Suspension bridge
Heavy
Expensive to build
Spans shorter range
Collapse in 1907 and 1916, twice!
Due to flaws in blueprint verification
Light weight
Cheap to build
Spans longer range
  Was the longest suspension bridge in the world!
Stands since 1970
Case-based testbench
Verification
Source: https://www.wikiwand.com/en/Quebec_Bridge#/google_vignette

## Slide 4: The Quebec Bridge and Pierre Laporte Bridge
Case-based testbench
Verification
Verbose
Hard and tedious to build
Provide limited test cases
Waveform eyeing
Ad-hoc
Concise
Easy to build
Powerful in test strength
  Coverage
  Constraints
  Randomization
  And many more
Formal methods to verify the results
True industry standard
Case-based testbench
Verification
Source: https://www.wikiwand.com/en/Quebec_Bridge#/google_vignette

## Slide 5: Intel’s Pentium FDIV bug
A hardware bug affecting the floating-point unit (FPU)
Discovered in 1994
Caused Intel about $ 0.5 billion to recall all flaw processors in 1995.
  Roughly speaking $ 0.5 billion in 1995 is worth $ 0.9 billion today
  ~7.4 billion SEK
  Ericsson full-year sales in 2020: ~70 billion SEK worldwide
Source: https://en.wikipedia.org/wiki/Pentium_FDIV_bug
Does this bug affect OS kernel space
such as Linux?

## Slide 6: More recently – Meltdown and Spectre
A hardware bug affecting branch prediction and speculative execution in modern CPU.
Discovered in 2018
Affecting almost all modern processors:
  Intel x86 microprocessors
  IBM POWER processors
  ARM-based microprocessors
  Not on AMD processors*
* https://en.wikipedia.org/wiki/Meltdown_(security_vulnerability)
Does this bug affect OS kernel space
such as Linux?

## Slide 7: Verification, validation, testing
In hardware design domain
  Verification = a process in which a design is tested (or verified) against a given design specification before tape-out.
  Validation = a process in which the manufactured design (chip) is tested for all functional correctness in a lab setup.
  Testing = screening manufactured chips for faults or random defects, reliability, functional defects and electrical characterization before volume shipment.
Specifications
Architecture
Microarchitecture
RTL Design
Physical Design
Tapeout
Prototype
(Chip back from fab)
Chip design and development life cycle
Verification (this lecture)
Validation
Testing
Volume shipment

## Slide 8: The Embedded SoC engineering pie
Chart: 
| System design | Implementation | Verification
Sales | 1 | 2 | 7

## Slide 9: What to verify – the reconvergence model
Remember that the purpose of the verification process is to ensure that the functionality of a logic is as intended.
The reconvergence model is a conceptual representation of what to verify.
Requirements
System design team’s interpretation
(SystemC)
Specification
Implementation
Design Team’s Interpretation
(Verilog)
Verification Team’s Interpretation
(SystemVerilog)
Do not fight.
Independence of interpretation by design and verification teams is expensive but essential.

## Slide 10: Verification models
Black-box model
  The verification team has access to input and output only
White-box model
  The verification team has access to the internal logic
Grey-box model
  The verification team has access to the internal logic that is specifically designed to aid debug

## Slide 11: Verification abstraction
Function/system level
  Operations ordered by functionality
  Example: DSP systems modeled in Matlab
Transaction level
  Operations ordered by transmission protocol
  Example: AXI data transfer
RTL/cycle accurate level
  Operations ordered by clock signal
  Example: FSM state transition
Gate/Transistor level
  Operations ordered by physical signal
  Example: Bit change in gate with manufactural delays
We mainly focus here
Higher abstraction level = greater efficiency but less control

## Slide 12: Verification tasks
In each of the verification hierarchy, checking the following
  Function and performance
    Function: A piece of HW/SW that transforms input to output
    Performance: How well does the function perform in terms of figures of merits
  Timing and interface
    The logic timing which specifies when the input and output should appear/be valid/be active, especially in relation to each other.
  Address/Location/Amount
    The amount of data that is read/input and the location from which it is read.
    The amount of data that is written/output and the location to which it is written.
  Structure/configuration
    IPs/Sub-systems are connected and configured properly

## Slide 13: The verification space
Model
Abstraction
Task

## Slide 14: Why SystemVerilog
Verilog lacks
  Constrained random generation
  Functional coverage
  Assertions
Specman E/Vera
  Used with VHDL and Verilog for constrained random generation and functional coverage
Property specification language (PSL)
  For assertion
Learning 1 language (SystemVerilog) is better than learning 2 (Specman E/Vera and PSL)
Even as a verification engineer, one should have enough knowledge on HDL and system design language such as SystemC

## Slide 15: More than just a verification tool
SystemVerilog rapidly getting accepted as the next generation HDL for
  System design
  RTL design and synthesis
  Verification
Easy bridging up different design teams.
It is strongly practiced by the industries such as Ericsson.
There are many properties and features in SV (can be enough for another full course).
We will only cover a small set of useful ones for writing testbench in this course.
In this course, we use Verilog for RTL modeling and SV only for verification.

## Slide 16: Basic building blocks
Basic data types
Different always blocks
Struct vs. Class
Packed and unpacked array
Associative array
File

## Slide 17: Basic data types
2 valued data type
  bit: 1 bit
  byte: 8 bit (char), signed
  shortint: 16 bit, signed
  int: 32 bit, signed
4 valued data types
  reg/wire: 1 bit
  logic: 1 bit, identical to reg
  integer: 32 bit, signed
bit [15:0] bus; //unsigned
bit signed [11:0] i, q; // signed
shortint unsigned addr_unsigned;
logic [15:0] addr_logic;
string myName = “John Smith”;
byte c = “A”; // assign c “A”
bit [3:0][7:0] s = “hello”; // assign s “ello”
$display("bus=%b", bus);
$display("i,q=%b", i);
$display("addr_unsigned=%b", addr_unsigned);
$display("addr_logic=%b", addr_logic);
$display("myName=%s", myName);
$display("c=%c", c);
$display("c=%b", c);
$display("s=%s", s);
//demo_1
Choose the proper data type to use in the testbench.

## Slide 18: Different always blocks
Comes in four flavors
  always
    The old Verilog legacy.
  always_ff
    Clocked synchronous body
    To infer DFF
    The only case to use “<=”
  always _comb:
    To infer combinational logic
    Sensitivity list is inferred from signals involved in the RHS of expressions.
  always_latch
    To infer latch
    Sensitivity list is inferred from signals involved in the RHS of expressions.
module demo_2(
input a,
input b,
output c
);
reg c;
always_comb
if (b)
c = a;
endmodule
module demo_2(
input a,
input b,
output c
);
reg c;
always_latch
if (b)
c = a;
endmodule
module demo_2(
input a,
input b,
output c
);
reg c;
always_ff
if (b)
c <= a;
endmodule
Compilation error.
Warning.
No comb logic generated
Correct.
always_ff @ (a, b)
if (b)
c <= a;
Warning.
No DFF generated.
Can be used for synthesis.

## Slide 19: Struct vs. Class
Both are used to represent information composed of different types.
The example struct models IEEE single-precision floating-point number.
The example class models ATM info packet which is fixed 4-byte of user data.
typedef struct {
bit sign;
bit [22:0] mantissa;
bit [ 7:0] exponent;
} ieee_sp_float;
class atm_pkt;
bit [11:0] id;
bit [15:0] pw;
bit [ 3:0] pri;
endclass: atm_ pkt
Pay attention to the difference of the semi-colon at the end

## Slide 20: Concept of struct
A struct is an integral type, just like integer or reg.
Whenever a “struct” type is declared, the necessary number of bits is automatically allocated.
If a struct variable is assigned to another or passed as an argument to a function or task, all the bits are copied.
typedef struct {
bit sign;
bit [22:0] mantissa;
bit [ 7:0] exponent;
} ieee_sp_float_unpacked

## Slide 21: Concept of struct
If a struct is declared packed, the bits of the struct fields are laid out consecutively in memory.
We can thus define literal value for a struct.
This allows the struct to be seamlessly converted to and from bit vectors.
typedef struct packed {
bit sign;
bit [22:0] mantissa;
bit [ 7:0] exponent;
} ieee_sp_float_packed
Sign
Mantissa
Exponent
31
30 6
5 0

## Slide 22: More on struct
module demo_3;
function ieee_sp_float_packed abs (ieee_sp_float_packed v);
v.sign = 0;
abs = v;
endfunction: abs
initial begin
ieee_sp_float_packed v1, v2;
ieee_sp_float_unpacked v3;
v1 = {1'b1, 23'hf00000, 8'h0};
v2 = v1;
v1 = abs(v1);
$display("v1 = %b, %b, %b", v1.sign, v1.mantissa, v1.exponent);
$display("v1 = %b, %b, %b", v1[31], v1[30:8], v1[7:0]);
$display("v2 = %b, %b, %b", v2[31], v2[30:8], v2[7:0]);
v3 = {1'b1, 23'hf00000, 8'h0};
$display("v3 = %b, %b, %b", v3.sign, v3.mantissa, v3.exponent);
$display("v3 = %b, %b, %b", v3[31], v3[30:6], v3[5:0]);
end
endmodule
Error
Warning
Concatenation assignment to unpacked struct leads to warning.
Bit selection on unpacked struct leads to compilation error.

## Slide 23: Concept of class
class atm_pkt;
bit [11:0] id;
bit [15:0] pw;
bit [ 2:0] pri;
function new (bit [11:0] id = 12’hfff,
bit [15:0] pw = 16’hffff);
this.id = id;
this.pw = pw;
this.pri = 3’b0;
endfunction
function atm_pkt copy ();
  copy = new;
  copy.id = this.id;
  copy.pw = this.pw;
  copy.pri = this.pri;
endfunction: copy
function display ();
$display (“ id = 0x%0h,
pw=0x%0h,
pri=%0b",
this.id, this.pw, this.pri);
endfunction
endclass: atm_pkt
In object-oriented programming (OOP), a class is a structure that encapsulates variables and functions that process the variables.
Some of the functions are pre-defined implicitly but can be override by user explicitly.
All other functions should be defined explicitly by user.
Overridden constructor new
Self-defined function
Self-defined function
Variable
By default, “public”
To use private var:
local bit [11:0] id
Call the overridden new constructor

## Slide 24: Instantiation of class using new
class atm_pkt;
bit [11:0] id;
bit [15:0] pw;
bit [ 2:0] pri;
function new (bit [11:0] id = 12’hfff,
bit [15:0] pw = 16’hffff);
this.id = id;
this.pw = pw;
this.pri = 3’b0;
endfunction
. . .
function display ();
$display (“ id = 0x%0h,
pw=0x%0h,
pri=%0b",
this.id, this.pw, this.pri);
endfunction
endclass: atm_pkt
module demo_4;
initial begin
atm_pkt u1, u2;
u1 = new;
u2 = new (12'h123, 16'h1234);
u1.display();
u2.display();
end
endmodule
Output from Vivado

## Slide 25: More on class
A class is a dynamic type.
Whenever a class type is declared (using the new keyword), only a null pointer to a new instance of the class is created.
All info of the instance must be explicitly allocated.
If a class variable is assigned to another or passed as an argument to a function or task, only the pointer is copied into another class instance.
class atm_pkt;
...
function new (bit [11:0] id = 12’hfff,
bit [15:0] pw = 16’hffff);
this.id = id;
this.pw = pw;
this.pri = 3’b0;
endfunction
function atm_pkt copy ();
copy = new;
copy.id = this.id;
  copy.pw = this.pw;
  copy.pri = this.pri;
endfunction: copy
…
endclass: atm_pkt
module demo_4
Initial begin
atm_pkt u1, u2, u3; // object instantiation
u1 = new;
u1.id = 12’h123;
u2 = u1; // u1 & u2 refer to same
// instance
u3 = u2.copy(); // u2 & u3 differ
// but have same content
u2.id = 12’h456; // only u1 and u2 will // change
end

## Slide 26: Difference between struct & class
A class can be converted to and from bit vectors by using user defined packing and unpacking functions.
The biggest difference between struct and class is that the class is the only type in SystemVerilog that supports the object-oriented programming model.
  Encapsulation
  Inheritance
  Polymorphism
Use struct for writing synthesizable design.
  Packed struct is very similar to bit-vectors
Use class when writing testbenches.
Learn at least one OOP language.
C++/Python/SystemC

## Slide 27: Packed and unpacked array
Packed arrays can only be made of single-bit types and their dimensions are specified to the left of the variable name.
  Packed arrays are implemented as consecutive bits and can be implicitly used as signed or unsigned integer values.
bit [ 7:0] a_byte;
logic [ 3:0] [ 7:0] q_quadword;
ieee_sp_float [31:0] scoreboard; // INVALID
Unpacked arrays can be of any type.
They are declared with their dimensions specified to the right of the variable name.
  Each element of an unpacked array is an individual value.
bit eight_bits[8];
logic sixteen_bits[4][4];
ieee_sp_float scoreboard[32]; // VALID

## Slide 28: More on unpacked array
Which should be used to model a general-purpose array?
  Packed or unpacked?
A dynamic array is an unpacked array with an unspecified dimension size.
  The actual size of the array is specified and allocated at runtime.
  1-D or multi-dimensional.
ieee_sp_float_packed array_1d [ ]; //demo_5
array_1d = new [32]; // 32 elements
array_1d = new [64] (array_1d); // resize
array_1d.delete(); // Delete array
ieee_sp_float_packed array_2d [ ][ ];
bit [22:0] rand_vec;
array_2d = new [32];
foreach (array_2d [i])
array_2d[i] = new [32];
foreach (array_2d [i, j])
rand_vec = $urandom();
array_2d[i][j] = {1'b1, rand_vec, 8'h0};
Call the SV operator new to allocate memory for the array dynamically.
Not a constructor!
Observe how the array_2d is indexed.
No need to declare I,j

## Slide 29: Multi-dimensional dynamic array of class
Multi-dimensional dynamic arrays can be emulated by using a dynamic array of classes containing a dynamic array.
Since this multi-dimensional array is composed of independent one-dimensional arrays, the size and number of each dimension can vary.
class pixel;
bit [7:0] red;
bit [7:0] green;
bit [7:0] blue;
endclass: pixel
/*******************************/
class line;
pixel pixels[];
function new (input int unsigned n);
this.pixels = new[n];
endfunction: new
endclass: line
/*******************************/
class picture;
line lines[];
function new (input int unsigned x,y);
this.lines = new [x];
foreach (this.lines[i]) begin
this.lines[i] = new(y);
end
endfunction: new
endclass: picture
module demo_3;
initial begin
picture vga = new(480, 640);
pixel center = vga.lines[240].pixels[320];
end
endmodule
Need to call new()!
Otherwise, only nulls exist in pixels
Problem?
foreach (this.pixels[i])
this.pixels[i] = new();

## Slide 30: Associative array
Associative arrays are used for non-ordinal or non-consecutive indexing operations.
  The elements in an associative array are not considered ordered from index 0 through index N-1.
  They are randomly stored based on an efficient indexing mechanism that can use any type — even a string or class reference — as indexing value.
  The concept is close to the “map” data structure
One of the best applications of an associative array is to model a large memory.
16GB
0
Allocated region

## Slide 31: More on associative array
class sparse_memory;
local logic [7:0] mem [bit [63:0]];
/********************************/
function logic [7:0] read(input bit [63:0] addr);
read = 8’hxx;
if (this.mem.exists(addr)) begin
read = this.mem[addr];
end
endfunction: read
/********************************/
function void write(input bit [63:0] addr,
input logic [ 7:0] data);
this.mem[addr] = data;
endfunction: write
/********************************/
function void display();
foreach (mem[i])
$display("Addr: 0x%h, data: 0x%h", i, mem[i]);
endfunction: display
endclass: sparse_memory
module demo_7;
sparse_memory mem = new();
bit [63:0] addr;
bit [7:0] data;
initial begin
$display(“Method 1 Init. memory by random writing”);
repeat (10) begin
addr = { $urandom(), $urandom() };
data = $urandom();
mem.write(addr, data);
$display("0x%h, 0x%h", addr, mem.read(addr));
end
mem.display();
end
endmodule
$random()/$urandom() only return 32-bit random number

## Slide 32: File
SystemVerilog can both open file for read and write using the $fopen() system task.
The task will return a 32-bit integer handle called a file descriptor. This handle should be used to read and write to the file until closed.
Close a file by using the $fclose() system task.
File is another way to initialization memory content.

## Slide 33: More on File
class sparse_memory; // demo_7
local logic [7:0] mem [bit [63:0]];
/********************************/
function void loadimage();
$display("Loading mem image...");
fd = $fopen("mem_image.txt", "r");
if (fd) begin
while (!$feof(fd)) begin
bit [63:0] addr;
bit [7:0] data;
string line;
$fgets(line, fd);
$sscanf(line, "%h %h", addr, data);
this.write(addr, data);
end
$fclose(fd);
end else
$display("Error in opening memory image file.");
endfunction: loadimage
endclass: sparse_memory
module demo_7;
sparse_memory mem = new();
bit [63:0] addr;
bit [7:0] data;
initial begin
$display(“Method 2 Load memory by reading file”);
mem.loadimage();
mem.display();
end
endmodule
Remember to import the file to Vivado as “Simulation Sources”
File content

## Slide 34: Questions?